Table 1. Operating conditions for anaerobic and aerobic BTFs degrading chlorform

| Operating condition | BTF Type | Phases |
| --- | --- | --- |
|  |  | I | II | III | IV |
| Influent Chloroform concentration, ppmv |  | 5 |
| Empty Bed Residence Time, min |  | 5 |
| Influent Ethanol concentration, ppmv |  | 25 | 50 | 100 | 200 |
| Operation time, days | Anaerobic | 44 | 33 | 41 | 35 |
|  | Aerobic | 30 | 29 | 122 | 33 |
| Average Chloroform Removal Efficiency (%) | Anaerobic | 49±9 | 52±7 | 56±7 | 59±10 |
|  | Aerobic | 69.9±9 | 71.6±5 | 75.1±9 | 80.9±4 |
| Loading Rate (g/m3. h) | Anaerobic | 0.27 | 0.27 | 0.27 | 0.27 |
|  | Aerobic |  |  |  |  |
| Elimination Capacity (g/m3. h) | Anaerobic | 0.13±0.02 | 0.14±0.01 | 0.15±0.02 | 0.16±0.01 |
|  | Aerobic | 0.21±0.01 | 0.22±0.01 | 0.22±0.01 | 0.23±0.01 |